## Slide 1: A DIGITAL HEARING AID
Ankur Agarwal(Y09UC216)
Hansraj Gujar(Y09UC233)
Neeraj Gupta(Y09UC254)
Shrey Upadhyay(Y09UC282)
Sumit Gautam(Y09UC285)

## Slide 2: INTRODUCTION
In this project, we developed noise reduction, frequency, and amplitude filters for a configurable digital hearing aid (DHA).
Why digital?
Analog hearing aids yield significant limitations due to
Inadequate spectral shaping
Narrow operating bandwidth
Partial noise-reduction capability
This leads to sub-optimal clarity and audibility restoration and sub-optimal speech perception in noisy environments.

## Slide 3: Working
The analog sound signal is converted into digital domain.
The digital signal processor(filters) manipulates the signal without causing any distortion, so sounds come through more clearly and speech is easier to hear and understand.

## Slide 4: Assumptions
The highest frequency that most humans can hear is approximately 20 kHz. Therefore, before the signal enters the A/D converter, it will be lowpass-filtered to 20 kHz, which is also our sampling frequency. This will avoid aliasing during sampling.
It does not operate in real-time, since we take in the entire speech signal and then manipulate it.

## Slide 5: Design
1.
2.

## Slide 6: Noise reduction filter
Assumptions
External signals or Noise can be modelled using white gaussian noise.
We used the command wdencmp, which performs noise reduction/compression using wavelets. It returns a de-noised version of the input signal using wavelet coefficients thresholding.

## Slide 7: Frequency shaper
The filter applies a gain greater than one to the frequencies that the user has difficulty hearing.
As one of its parameters, the filter takes in a vector of frequencies, that define the user's hearing characteristics.
For each range, the frequency shaper applies a certain gain based on the user's specific hearing characteristics . Thus, our frequency shaper is completely configurable to any user.

## Slide 8: Amplitude shaper
Once the signal has been passed through the Noise Reduction Filter and the Frequency Shaper, it will be passed through our Amplitude Shaper .
We assume that the Frequency Shaper raises the frequencies that the user has difficulty hearing to sound pressure levels within his dynamic range of hearing.
Therefore, all that our Amplitude Shaper has to do is check, bit by bit, that output power does not exceed a given saturation level, Psat.

## Slide 9
Since noise is concentrated in the low power levels as well, the filter also removes a significant amount of noise. Output power is equal to zero for levels below Psat.

## Slide 10: Conclusion
We successfully modeled a digital hearing aid in MATLAB by implementing a noise reduction filter, frequency shaper and an amplitude shaper for a given speech signal.